## Slide 1: Permanent Magnet Synchronous Motor control
21/06/2024
Daniel Montesinos-Miracle (daniel.montesinos@upc.edu)
Oriol Subirats-Rillo (oriol.subirats.rillo@upc.edu)

## Slide 2: Agenda
 | TEMA – CONTENIDO | MATERIAL DE ESTUDIO – METODOLOGÍA
Duración: 1 h Prof.: Daniel Montesinos | Introducción. Generación de par. Motor DC como ejemplo Motores PMSM (o BLAC) y BLDC. Fuerza contraelectromotriz | Sesión teórica para introducir las bases de la generación de par en máquinas eléctricas rotativas y presentar las estrategias de control de este tipo de máquinas. Ejemplo del motor DC. Diferencias entre BLDC y PMSM.
Duración: 3 h Prof.: Daniel Montesinos | Modelado y control del motor PMSM. | Sesión teórica-práctica para abordar los aspectos del modelado y estrategias de control del motor PMSM. En la práctica se implementará el modelo y el control de par y velocidad del motor PMSM usando la herramienta PLECS.
Duración: 2 h Prof.: Daniel Montesinos/Oriol Subirats | Convertidores para motores PMSM. Estrategias de modulación | Sesión teórica-práctica para presentar las distintas estrategias de modulación para motores PMSM. En la práctica se implementará una de las estrategias de modulación como proceso incremental del modelado del sistema iniciado en la sesión anterior.
Duración: 2 h Prof.: Oriol Subirats | Operación en la zona LBEF. Operación en la zona FW | Sesión teórica-práctica en la que se desarrolla el modelo para analizar los puntos de trabajo del motor y seguidamente se analiza la operación en la zona LBEF y FW. En la parte práctica se implementará en el modelo de simulación incremental la operación en la región de operación en Field-Weakening
Duración: 1 h Prof.: Oriol Subirats | Obtención práctica de parámetros de un motor PMSM | En esta sesión se explicará cómo se pueden obtener los parámetros del motor PMSM necesarios para el diseño de un sistema de control FOC.
Duración: 1 h Prof.: Oriol Subirats | Aspectos para el control digital de convertidores | Sesión teórica en donde se darán las indicaciones básicas para la implementación de controladores digitales para convertidores de potencia.

## Slide 3: Mechanical system to control
Main objective: desired position/speed/torque profile
Secondary objectives
  Load, drive and people protection
  Reliability, robustness

## Slide 4: Energy flow
Traction phase
Braking phase

## Slide 5: Types of loads
Constant torque: hoist, tyre friction, weight
Linear load: compressor
Quadratic load: fan, wind turbine, air friction
Constant power: winder

## Slide 6: Ideal power plant
Constant power profile over speed
Limited torque at low speeds due to maximum tractive effort, maximum current
Limited speed due to mechanical or electrical limitations
Constant torque during rotation to avoid vibration, noise and fatigue

## Slide 7: Forces in a vehicle
Fa: aerodynamical drag
Fr: Rolling friction
Fg: weight
Ft: tractive force
m

## Slide 8: NEDC driving cycle

## Slide 9: Driving profile – force profile

## Slide 10: Lab0. VEHICLE MODEL

## Slide 11: Forces in a vehicle
Fa: aerodynamical drag
Fr: Rolling friction
Fg: weight
Ft: tractive force
m

## Slide 12: Aerodynamic friction losses
Two origins
  Viscous friction of surrounding air
  Pressure difference in front and rear
  r: air density
  Af: frontal area
  cd: aerodynamic drag coefficient
  V: vehicle speed
  Vw: wind speed

## Slide 13: Aerodynamic drag coeficient

## Slide 14: Rolling friction
Due to hysteresis of tire material

## Slide 15: Rolling friction
Depends on many factors: vehicle speed, tyre pressure, road surface conditions
  fr: rolling friction coefficient
  M: vehicle mass
  g: gravity constant
  a: road slope
Accepted speed dependence for most situations

## Slide 16: Hill climbing force
Conservative
Great influence on vehicle dynamics
  M: vehicle mass
  g: gravity constant
  a: road slope

## Slide 17: Parameters
Environment
Parameter | Value
Vehicle mass (mv) | 150 kg
Drag coeficient (Cd) | 0,85
Frontal area (Af) | 0,4 m2
Rolling resistance coeficient (fr) | 0,025
Tyre effective rolling radius (rw) | 0,06 m
Reduction gear (kgear) | 10
Vehicle
Parameter | Value
Air density (r) | 1,22521 kg/m3
Gravity constant (g) | 9,8 m/s2
Air speed | 0 m/s
Grade | 0 %

## Slide 18: DC motor

## Slide 19: Torque production

## Slide 20: Torque production. DC motor
https://www.youtube.com/watch?v=CWulQ1ZSE3c

## Slide 21: DC motor torque production
On a wire carrying electric current placed in a magnetic field (armature), a magnetic force acting on the wire is produced

## Slide 22: Effect of the number of windings

## Slide 23: Constant torque

## Slide 24: Back electromotive force
A variable time flux linkage induces a voltage in a winding (back emf). Lenz or Faraday law

## Slide 25: DC motors
Easy to control torque/speed
Widely known
Low-cost
Low power (200 W)
Low efficiency (70 %)
High maintenance (brushes)

## Slide 26: DC motor dynamic model and equations

## Slide 27: DC steady state motor model and equations

## Slide 28: Example
DC motor parameters
Speed, current and torque performance

## Slide 29: Operating points – steady state

## Slide 30: Operating points – steady state

## Slide 31: Heat and thermal characteristics
-

## Slide 32: Heat and thermal characteristics

## Slide 33: Safe Operating Area
1
2
2
4
3
1
Commutation limit
t = 1’
t = 20’
t = 60’
Continuos Duty
The maximum torque, current or power can be limited by the converter

## Slide 34: control

## Slide 35: DC motor dynamic model and equations

## Slide 36: Step response
Values
  Ua = 300 V
  TL = 372 Nm
  J = 7,12 kg m2
  b = 7,2 N s rad-1
  Ra = 25 mW
  La = 2 mH
  K = 3,72 V·s/rad

## Slide 37: Closed loop system

## Slide 38: Controller tuning

## Slide 39: Internal Model Control
tr is the settling time from 10% to 90%
Kp and Ki impose these dynamics in a first-order system
tr

## Slide 40: PI saturation
The output of the current PI controller is the voltage to be applied to the motor
The motor voltage is limited to protect the motor, but limits the maximum speed
And the integrator continues to integrate the error
Anti wind-up to reset faster the saturated integrator output

## Slide 41: Anti wind-up PI controller

## Slide 42: Power Electronics for DC motor

## Slide 43: 4 quadrant converter
Now the car accelerates and brakes in both senses

## Slide 44: Basic equations

## Slide 45: Lab1. DC motor model and control

## Slide 46: Motor parameters Maxon RE 65, 250 W, 48 V
Parameter | Value
Rated power (P) | 250 W
Rated voltage (V) | 48 V
Rated current (A) | 6,8 A
Rated speed (rpm) | 3420 rpm
Maximum speed (rpm) | 6000 rpm
EMF constant (kF) | 77,8 rpm/V
Winding resistance (ra) | 0,365 W
Winding inductance (La) | 0,161 mH

## Slide 47: Ac motors

## Slide 48: AC brushless motors

## Slide 49: Constant torque

## Slide 50: AC motors
Higher power ( +100 kW)
Low-maintenance (no brushes)
Higher efficiency ( 98 %)
Internal o external rotor
Rare earth magnets
More complex control
Needs position sensor
Needs for power electronics

## Slide 51: AC motors
Used for traction or high power
Mainly two types: PMSM and Induction
Also synchronous reluctance motor (SyncRel) and Switched Reluctance Motor
Need of power electronics and complex control

## Slide 52: Brushless DC motor

## Slide 53: Brushless DC motors
Higher power ( 10 kW)
Low-maintenance (no brushes)
Higher efficiency ( 90 %)
Internal o external rotor
Many shapes
Rare earth magnets
More complex control
Needs position sensor
Needs for power electronics

## Slide 55: Three phase inverter
Only two phases are used. The third phase is led unconnected (open switches)
Standard PWM as a DC motor
No current on the unconnected phase. Voltage = bemf. Sensorless methods are based on measuring this phase voltage

## Slide 56: Model and control of BLDC motors
As three equal DC motors
The model can be seen as a DC motor
Not using the full power capability of three phases

## Slide 57: Control of BLDC motors
The control is similar to a DC motor, but the commutation sequencer decides which of the two phases have to be excited. Synchronous motor

## Slide 58: Permanent Magnet Synchronous Motors - PMSM
Three sinusoidal distributed windings
Spatial shifted 120o
The magnet flux generates three sinusoidal voltages 120o in phase
No thermal effect on windings and magnet
No saturation on inductances

## Slide 59: Constant torque required
The magnet flux rotates with the rotor
To produce a constant torque, the stator flux must rotate at the same speed as rotor -> synchronous

## Slide 60: Sinusoidal currents
The stator flux must rotate
Three sinusoidal currents in stator

## Slide 61: Classification of permanent magnet synchronous motors
o BLAC

## Slide 62: Classification of PMSM
Rotor cross-section of different sinusoidal permanent magnet synchronous machines.
SPMSM
(Neodymium)
IPMSM
Radially magnetized
IPMSM
Tangentially magnetized
Inductance equation:
Reluctance equation:

## Slide 64: Performance of PMSM
Higher power (density) ( +100 kW)
Low-maintenance (no brushes)
Higher efficiency ( 98 %)
Internal or external rotor
High torque/inertia
High reliability
Rare earth magnets. High cost
More complex control
Needs position sensor
Needs for power electronics

## Slide 65: Permanent Magnet Synchronous Motors - PMSM
Three sinusoidal distributed windings
Spatial shifted 120o
The magnet flux generates three sinusoidal voltages 120o in phase
No thermal effect on windings and magnet
No saturation on inductances

## Slide 66: Electrical equations

## Slide 67: Electrical equations

## Slide 68: Electrical equations

## Slide 69: Electrical equations

## Slide 70: Classification of PMSM

## Slide 71: Electrical equations

## Slide 72: Electrical equations
Non-linear differential system
Some terms depend on the angle
Difficult to compute the torque
No able for analysis

## Slide 73: Constant torque required
The magnet flux rotates with the rotor
To produce a constant torque, the stator flux must rotate at the same speed as rotor -> synchronous

## Slide 74: Sinusoidal currents
The stator flux must rotate (at the same speed of the rotor)
Three sinusoidal currents in the stator

## Slide 75: Matrix transformations
is is a vector in a flat surface -> only two components needed (ia and ib)
This is the Clarke transformation
Star connected motor and isolated neutral

## Slide 76: Matrix transformations
Constant module (Clarke)
Orthogonal transformation. Maintains the instantaneous power (Concordia)

## Slide 77: Clarke transformation
From a three-phase system at 120o in a flat surface to an orthogonal three-phase system
But, the transformed variables still depend on the angle
Clarke

## Slide 78: Matrix transformations
ia y ib still depends on electrical rotor angle qr
To eliminate this dependence, a and b axes must turn with rotor flux
The rotating a and b axes are dr and qr

## Slide 79: Park transformation
Multiplying the two transformations

## Slide 80: Matrix transformations
Clarke
Rotation

## Slide 81: Park transformation
Constant module
Orthogonal transformation. Maintains the instantaneous power

## Slide 82: Park transformation of electrical motor equations

## Slide 83: Park transformation of electrical motor equations

## Slide 84: Park transformation of electrical motor equations
No angle dependent terms
Voltages and currents are DC values in steady state. Not sinusoids
Easy equation system
Easy to compute the produced torque

## Slide 85: Equivalent equations and circuit

## Slide 86: Produced torque expression

## Slide 87: Torque properties
The torque depends only from machine parameters and currents
The torque is proportional to ids and iqs
Two torques: magnet torque and reluctant torque

## Slide 88: The complete model

## Slide 89: Vector control
Torque expression for PMSM
Controlling and it is possible to control the current vector, the flux vector and the torque

## Slide 90: Vector control of PMSM

## Slide 91: Current control
Controls the current, controlling the produced torque
Direct limitation of current. Overload protections
Better dynamic performance
Low influence on parameter variation (rs, L,…)
Compensation of voltage drops due to semiconductors and dead time
Compensation of DC bus fluctuations
Without amplitude and phase error
Commutation frequency constant or limited
Low current harmonic injection in the motor
Efficient user of DC bus voltage

## Slide 92: Motor model and coupling terms
Currents and are DC values in steady state
But there is a cross coupling between d and q axes
It is not possible to independently control the currents
A variation on modifies and vice versa
That degrades the dynamic response
PI controllers can offer good performance, but decoupling is needed

## Slide 93: Decoupling of torque loops

## Slide 94: Speed loop
The mechanical system imposes the speed dynamics
The torque loop has a faster time constant
The torque loop is supposed to perfect control the required torque -> unitary gain

## Slide 95: Complete scheme for vector control

## Slide 96: Particular case: SPMSM
In an SPMSM Ld=Lq
The control strategy is to control iq to control the torque and control id=0. It minimized losses.
No reluctant torque

## Slide 97: inverters

## Slide 98: Inverters. DC/AC converters
Connect a DC voltage source with an AC current source. Three-phase and single phase

## Slide 99: Single phase inverter
Cell T1/T2 |  | Cell T3/T4 |  | Voltage us
T1 | T2 | T3 | T4 | 
On | Off | On | Off | Ue
On | Off | Off | On | 0
Off | On | On | Off | 0
Off | On | Off | On | -Ue

## Slide 100: Constant duty cycle modulation: two level
 | T1 | T2 | T3 | T4 | UA1 | UA2 | us
Ucm>uh | On | Off | On | Off | Ue | 0 | Ue
Ucm<uh | Off | On | Off | On | 0 | Ue | -Ue

## Slide 101: Constant duty cycle modulation: three level
T1 | T2 | T3 | T4 | UA1 | UA2 | us
On | Off | Off | On | Ue | Ue | 0
On | Off | On | Off | Ue | 0 | Ue
Off | On | Off | On | 0 | Ue | -Ue
Off | On | On | Off | 0 | 0 | 0

## Slide 102: Two level PWM modulation

## Slide 103: Three level PWM modulation

## Slide 104: Three level PWM modulation at double frequency

## Slide 105: Three phase inverters
Connect a DC voltage source to an AC current source

## Slide 106: Three phase inverter

## Slide 107: Six step modulation

## Slide 108: Sinusoidal PWM

## Slide 109: Space Vector Modulation
Based on vector representation of possible voltage converter vectors
3 half bridges, 2 possible states per bridge. A total of 8 combinations possible
8 possible voltage vector synthesizable by the converter

## Slide 110: Voltages

## Slide 111: Possible states
us10 | us20 | us30 | us1 | us2 | us3 | ussa | ussb | us | rs
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | ...
0 | 0 | Ue | -Ue/3 | -Ue/3 | 2Ue/3 | -Ue/3 | -Ue/√3 | 2Ue/3 | -2p/3
0 | Ue | 0 | -Ue/3 | 2Ue/3 | -Ue/3 | -Ue/3 | Ue/√3 | 2Ue/3 | 2p/3
0 | Ue | Ue | -2Ue/3 | Ue/3 | Ue/3 | -2Ue/3 | 0 | 2Ue/3 | p
Ue | 0 | 0 | 2Ue/3 | -Ue/3 | -Ue/3 | 2Ue/3 | 0 | 2Ue/3 | 0
Ue | 0 | Ue | Ue/3 | -2Ue/3 | Ue/3 | Ue/3 | -Ue/√3 | 2Ue/3 | -p/3
Ue | Ue | 0 | Ue/3 | Ue/3 | -2Ue/3 | Ue/3 | Ue/√3 | 2Ue/3 | p/3
Ue | Ue | Ue | 0 | 0 | 0 | 0 | 0 | 0 | ...

## Slide 112: Voltages hexagon

## Slide 113: Voltage limitation – PI saturation

## Slide 114: Duty cycle computation
From the two next vectors and zero vectors, the reference voltage must be computed

## Slide 115: Practical implementation
Sector selection
Duty cycle computation
Zero vector computation. Symmetrical 0 and 7 states

## Slide 116: Practical implementation
On-times for three phase PWM generator

## Slide 117: Bibliography
I. Husain, Electric and Hybrid vehicles. Design fundamentals, CRC Press,2003.
M. Ehsani, Y. Gao y A. Emadi, Modern Electric, Hybrid Electric and Fuel Cell Vehicles. Fundamentals, theory and design, CRC Press 2010.
J. Larminie y J. Lowry, Electric Vehicle Technology Explained, John Wiley & Sons Ltd, 2003.
John M. Miller, Propulsion systems for hybrid vehicles, The institution of electrical engineers, 2010.
P. Barrade, Electronique de puissance, Presses polytechniques et universitaires romandes, 2006
Mohan, Undeland and Robbins, Power electronics. Converterters, applications and design, Wiley.
S. Buso y P. Mattavelli, Digital control in power electronics, Morgan & Claypool, 2006.
P. D. Chandana Perera, Sensorless Control of Permanent-Magnet Synchronous Motor Drives, PhD Dissertation, 2002
C. Miguel-Espinar, Enhanced Flux-Weakening Control Algorithm for Permanent Magnet Synchronous Machines, PhD dissertation, 2023.